## Slide 1
Unit-3 Syllabus
Combinational logic and arithmetic circuit 6 6
Encoders and Decoders, Multiplexers and Demultiplexers, Adder, subtractors, comparators, introduction to Programmable Logic Devices (PLDs) like FPGA, Overview of IC classification.

## Slide 2
The digital systems in general are classified into two categories namely:
  Combinational logic circuits
  Sequential logic circuits.
Classification of Digital Circuits

## Slide 3
Identify number of Input & Output .
Construct Truth Table.
Write Logical Expression in SOP and POS Form.
Minimize Logical Expression.
Implement Logic Circuits.
Combinational Circuits

## Slide 4
Following are the examples of some combinational circuits:
  Half Adder, Full Adder
  Half Subtractor, Full Subtractor
  Multiplexers, Demultiplexers
  Encoders, Decoders
  Comparator & Code Converters
Examples of Combinational Circuits

## Slide 5
Adder
An Adder is a combinational circuit in digital electronics that performs binary addition.
    It takes two or more binary numbers as input.
    Produces the sum and sometimes a carry as output.
    Adders are the basic building blocks in ALU (Arithmetic Logic Unit), processors, and calculators.
Types of Adders
Half Adder (HA)
Full Adder (FA)

## Slide 6
Half Adder (HA)
A Half Adder is the simplest combinational circuit in digital electronics that adds two single-bit binary numbers.
It has:
Inputs → 2 (A, B)
Outputs → 2 (Sum, Carry)

## Slide 7
HA-Truth Table
Step-1: Identify the Input and Output Variables
Step-2: Draw the Truth Table

## Slide 8
HA-K Maps
Step-3: Draw K-Map using Truth Table & determine the simplified Boolean Expression

## Slide 9
HA-Logic Diagram

## Slide 10
HA-Limitations
Limitation of Half Adder
  It cannot perform addition when there is an input carry from a previous stage.
  That’s why we need a Full Adder for multi-bit addition.
✅ In short:
A Half Adder adds two binary inputs (A, B).
Outputs: Sum = A ⊕ B, Carry = A · B.
Built using XOR and AND gates.
Useful for simple 1-bit addition but cannot handle carry input.

## Slide 11
Full Adder (FA)
A Full Adder is a combinational logic circuit that performs the addition of three input bits:
A → First input
B → Second input
Cin → Carry input (from a previous addition stage)
It produces two outputs:
Sum (S)
Carry-out (Cout)
👉 Unlike the Half Adder, the Full Adder can handle carry input, making it suitable for multi-bit addition.

## Slide 12
FA-Truth Table
Step-1: Identify the Input and Output Variables
Step-2: Draw the Truth Table

## Slide 13
FA-K Map
Step-3: Draw K-Map using Truth Table & determine the simplified Boolean Expression

## Slide 14
FA-Logic Diagram

## Slide 15
Cont…
Advantages
Supports carry input.
Building block for multi-bit adders.
Widely used in ALUs, CPUs.
Can be built using simple Half Adders.
Limitations
Slower for large bit operations (carry delay).
More hardware complexity than Half Adder.
Limited to binary addition.

## Slide 16
Half Subtractor (HS)
A Half Subtractor is a combinational logic circuit used to perform the subtraction of two binary digits. It has two inputs and two outputs:
Inputs → A (minuend) and B (subtrahend)
Outputs → Difference (D) and Borrow (B)
It is called "half" because it cannot handle borrow input from a previous stage.

## Slide 17
HS-Truth Table
Step-1: Identify the Input and Output Variables
Step-2: Draw the Truth Table

## Slide 18
HS-K Map
Step-3: Draw K-Map using Truth Table & determine the simplified Boolean Expression

## Slide 19
HS-Logic Diagram
Step-4: Draw the Logic Diagram

## Slide 20
HA-Limitations
Half subtractors do not take into account "Borrow-in" from the previous circuit.
This is a major drawback of half subtractors.
This is because real time scenarios involve subtracting the multiple number of bits which can not be accomplished using half subtractors.

## Slide 21
Half Subtractor (HS)
Full Subtractor is a combinational logic circuit.
It is used for the purpose of subtracting two single bit numbers.
It also takes into consideration borrow of the lower significant stage.
Thus, full subtractor has the ability to perform the subtraction of three bits.
Full subtractor contains 3 inputs and 2 outputs (Difference and Borrow) as shown below:

## Slide 22
FS-Truth Table
Step-1: Identify the Input and Output Variables
Step-2: Draw the Truth Table

## Slide 23
HS-K Map
Step-3: Draw K-Map using Truth Table & determine the simplified Boolean Expression

## Slide 24
HS-Logic Diagram
Step-4: Draw the Logic Diagram

## Slide 25
Cont…

## Slide 26
MUX & DEMUX

## Slide 27
The term Multiplexer means many into one.
A Digital Multiplexer (MUX) is a combinational Circuit with more than One Input Lines, One output lines and more than one select lines.
A Multiplexer is a Digital Switch, also called a Data Selector.
It allows the binary information from several input lines or sources and depending on the set of select lines, particular input line, is routed onto a single output line.
Multiplexer (Data Selectors)
What are multiplexers? Draw the logical circuits and describe its working.

## Slide 28
MUX directs one of the inputs to its output line by using a control bit word (selection line) to its select lines.
Multiplexer contains the followings:
Cont…
              Data Inputs
              Selection Inputs
              A Single Output
Selection input determines the input that should be connected to the output.
The multiplexer acts like an electronic switch that selects one from different.

## Slide 29
Cont…

## Slide 30
The block schematic of a 2 : 1 multiplexer is shown below:
It has two data inputs Do and D₁, one select input S, an enable input E and one output Y.
The truth table of this MUX is shown below:
2:1Multiplexer
Draw the symbol and write truth table of 2:1 MUX
D1
D0

## Slide 31
Cont…
Enable | Select Input S | Output Y
0 | X | 0
1 | 0 | D0
1 | 1 | D1
When enable i/p is high then only works.

## Slide 32
4:1Multiplexer
Fig. shows the block diagram of a 4: 1 multiplexer and Table gives its truth table.
Note that n = 4 hence number of select lines i.e. m = 2 so that 2 = n.
The truth table tells us that if S₁ So 00, the data bit Do is selected and routed to output Y = Do
Similarly if S₁ So 01, then D₁ is selected and routed to the output Y = D₁
Y = D₂ for S₁ So = 10 and Y = D3 for S₁ So 11

## Slide 33
Cont…
This expression can be realized using basic gates as shown in

## Slide 34
8:1Multiplexer

## Slide 35
The block diagram of an 8 1 MUX is shown in Fig. 1and its truth table is shown in Fig. 2. It has eight data inputs, one enable input, three select inputs and one output.
Operating principle :
When the strobe or enable input is 0, the multiplexer will be 0 irrespective of any input. With E = 1, we can select any one of the eight data inputs and of the connect it to the output.
For example if S₂ S, So = 0 1 1 then the data input D, is selected and output Y will follow the selected input D3.
Realization using gates :
The expression for output Y can be obtained from the truth table of Fig. as
The realization of 8 : 1 MUX using gates is shown in Fig.
Cont…

## Slide 36
Cont…

## Slide 37: 8:1 Multiplexer using 4:1 Multiplexer
4:1
Mux
E
Y1
D0
D1
D2
D3
S0
S1
4:1
Mux
E
D4
D5
D6
D7
S0
S1
S1
S0
S2
Y2
Output
2:1
Mux
E
Y
D0
D1

## Slide 38: 8:1 Multiplexer using 4:1 Multiplexer
Select
Lines
4:1
Mux
E
Y1
D0
D1
D2
D3
S0
S1
Output
4:1
Mux
E
D4
D5
D6
D7
S0
S1
S1
S0
S2
Y2
Y

## Slide 39: 16:1 Multiplexer
Select Lines
Output
16:1
Mux
E
Enable Input
Y
D0
D1
Data
Inputs
Block Diagram
D2
D3
S0
S2
D4
D5
D6
D7
S1
D8
D9
D10
D11
D12
D13
D14
D15
S3

## Slide 40: 16:1 Multiplexer
Truth Table
Enable | Select Lines |  |  |  | Output
E | S3 | S2 | S1 | S0 | Y
0 | X | X | X | X | 0
1 | 0 | 0 | 0 | 0 | D0
1 | 0 | 0 | 0 | 1 | D1
1 | 0 | 0 | 1 | 0 | D2
1 | 0 | 0 | 1 | 1 | D3
1 | 0 | 1 | 0 | 0 | D4
1 | 0 | 1 | 0 | 1 | D5
1 | 0 | 1 | 1 | 0 | D6
1 | 0 | 1 | 1 | 1 | D7
1 | 1 | 0 | 0 | 0 | D8
1 | 1 | 0 | 0 | 1 | D9
1 | 1 | 0 | 1 | 0 | D10
1 | 1 | 0 | 1 | 1 | D11
1 | 1 | 1 | 0 | 0 | D12
1 | 1 | 1 | 0 | 1 | D13
1 | 1 | 1 | 1 | 0 | D14
1 | 1 | 1 | 1 | 1 | D15

## Slide 41
Some of the important applications of a multiplexer are as follows:
It is used as a data selector to select one out of many data inputs.
It is used for simplification of logic design.
In the data acquisition system. In designing the combinational circuits.
In the D/A converters.
To minimize the number of connections in a logic circuit.
Applications of a Multiplexer

## Slide 42
The De-Multiplexer is a combinational logic circuit that performs the reverse operation of multiplexer (Several output lines, one input line).
De -Multiplexer means one to many.
A De-Multiplexer is a circuit with one input and many output. By applying control signal, we can steer any input to the output. Few types of De -Multiplexer are 1-to 2, 1-to-4, 1-to-8 and 1-to 16 De -Multiplexer .
De-Multiplexer is the process of taking information from one input and transmitting the same over one of several outputs.
De-Multiplexer

## Slide 43
A demultiplexer performs the reverse operation of a multiplexer i.e. it receives one input and distributes it over several outputs.
At a time only one output line is selected by the select lines and the input is routed to the selected output line.
Hence a demultiplexer is equivalent to a single pole multiple way switch as shown in Fig.
Cont…

## Slide 44
Similar to the multiplexers, the demultiplexers are classified as follows:
1:2 demultiplexer
1:4 demultiplexer
1:8 demultiplexer
1: 16 demultiplexer
Types of Demultiplexers

## Slide 45
1:2 Demux

## Slide 46
1:4 Demux

## Slide 47: 1: 8 De-multiplexer
Select Lines
1:8
De-mux
E
Enable
Input
Y0
Y1
Data
Input
Block Diagram
Din
S0
S1
Y2
Y3
Y4
Y5
Y6
Y7
S2

## Slide 48: 1: 8 De-multiplexer
Enable i/p | Select i/p |  |  | Outputs |  |  |  |  |  |  | 
E | S2 | S1 | S0 | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0
0 | X | X | X | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Din
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | Din | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | Din | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | Din | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | Din | 0 | 0 | 0 | 0 | 0 | 0 | 
Truth Table

## Slide 49: 1: 16 De-multiplexer
1:16
De-mux
E
Enable
Input
Y0
Data
Input
Block Diagram
Din
S0
S1
S2
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
S3

## Slide 50: De-mux Tree
Similar to multiplexer we can construct the de-multiplexer with more number of lines using de-multiplexer having less number of lines. This is call as “De-mux Tree”.

## Slide 51: 1:4 De-mux using 1:2 De-mux
Select
Lines
1:2
De-mux
E
Y0
Y1
S0
Data
Input
Din
1:2
De-mux
E
Y2
Y3
Din
S1
S0
S0
Y0
Y1
Y0
Y1

## Slide 52: 1:16 De-mux using 1:4 De-mux
Y0
Y1
Y2
Y3
S0
S1
S0
S1
S0
S1
S0
S1
1:4
De-mux
S0
S1
S2
S3
Data
Input
Y0
S1
S0
Y1
Y2
Y3
Din
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
Din
Din
Din
Din
1:4
De-mux
1:4
De-mux
1:4
De-mux
1:4
De-mux

## Slide 53
Applications of Multiplexer
Communication system – Communication system is a set of system that enable communication like transmission system, relay and tributary station, and communication network. The efficiency of communication system can be increased considerably using multiplexer. Multiplexer allow the process of transmitting different type of data such as audio, video at the same time using a single transmission line.
Computer Memory – A Multiplexer is used in computer memory to keep up a vast amount of memory in the computers, and also to decrease the number of copper lines necessary to connect the memory to other parts of the computer.

## Slide 54
Applications of De-Multiplexer
Communication System - Communication system use multiplexer to carry multiple data like audio, video and other form of data using a single line for transmission. This process make the transmission easier. The demultiplexer receive the output signals of the multiplexer and converts them back to the original form of the data at the receiving end. The multiplexer and demultiplexer work together to carry out the process of transmission and reception of data in communication system.

## Slide 55: 74153 Multiplexer IC
Specifications :
TTL ICs i.e. Transistor Transistor Logic ICs.
Total pins = 16 pins.
Dual 4:1 line multiplexer circuit in single package.
Supply voltage = 5V DC ±0.25V.
Operating temperature range = 0°C to +70°C.
High fan-out = 10.
Low impedance < 100Ω
Totem pole outputs.

## Slide 56: Decoder
Decoder is a combinational circuit.
It converts n bit binary information at its input into a maximum of 2n output lines.
For example, if n=2 then we can design upto 2:4 decoder

## Slide 57: 2:4 Decoder
2:4
Decoder
E
Enable
Input
Y0
Y2
Inputs
Block Diagram
A
Truth Table
B
Y1
Y3
Enable i/p | Data Inputs |  | Outputs |  |  | 
E | A | B | Y0 | Y1 | Y2 | Y3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 58: De-multiplexer as Decoder
It is possible to operate a de-multiplexer as a decoder.
Let us consider an example of 1:4 de-mux can be used as 2:4 decoder

## Slide 59: 1:4 De-multiplexer as 2:4 Decoder
Select Lines
1:4
De-mux
E
Enable
Input
Y0
Y1
Data
Input
Din
S0
S1
Y2
Y3
1:4
De-mux
E
Enable
Input
Y0
Y2
Inputs
A
B
Y1
Y3
S1
S0
Din
Vcc
1: 4 De-multiplexer
1: 4 De-multiplexer as 2:4 Decoder

## Slide 60: Realization of Boolean expression using De-mux
We can implement any Boolean expression using de-multiplexers.
It reduces circuit complexity.
It does not require any simplification

## Slide 61: Example 1
Since there are three variables, therefore a de-multiplexer with three select input is required i.e. 1:8 de-multiplexer is required
The 1:8 de-multiplexer is configured as below to implement given Boolean expression
Implement following Boolean expression using de-multiplexer

## Slide 62: Example 1 continue…..
+Vcc
1:8
De-mux
E
Enable
Input
Y0
Y1
Data
Input
Din
S0
S1
Y2
Y3
Y4
Y5
Y6
Y7
S2
A
B
C
Y

## Slide 63: Example 2
Since there are four variables, therefore a de-multiplexer with four select input is required i.e. 1:16 de-multiplexer is required
The 1:16 de-multiplexer is configured as below to implement given Boolean expression
Implement following Boolean expression using de-multiplexer

## Slide 64: Example 2 continue…..
A
B
C
+Vcc
D
1:16
De-mux
E
Enable
Input
Y0
Data
Input
Din
S0
S1
S2
Y1
Y2
Y3
Y4
Y5
Y6
Y7
Y8
Y9
Y10
Y11
Y12
Y13
Y14
Y15
S3
Y

## Slide 65: Multiplexer ICs
IC Number | Description | Output
IC 74157 | Quad 2:1 Mux | Same as input
IC 74158 | Quad 2:1 Mux | Inverted Output
IC 74153 | Dual 4:1 Mux | Same as input
IC 74352 | Dual 4:1 Mux | Inverted Output
IC 74151 | 8:1 Mux | Inverted Output
IC 74152 | 8:1 Mux | Inverted Output
IC 74150 | 16:1 Mux | Inverted Output

## Slide 66: De-multiplexer ICs
IC Number | Description
IC 74138 | 1:8 De-multiplexer
IC 74139 | Dual 1:4 De-multiplexer
IC 74154 | 1:16 De-multiplexer
IC 74155 | Dual 1:4 De-multiplexer

## Slide 67: Encoder
Encoder is a combinational circuit which is designed to perform the inverse operation of decoder.
An encoder has ‘n’ number of input lines and ‘m’ number of output lines.
An encoder produces an m bit binary code corresponding to the digital input number.
The encoder accepts an n input digital word and converts it into m bit another digital word

## Slide 68: Encoder
.
.
.
.
.
.
‘n’
inputs
‘m’
outputs
Encoder

## Slide 69: Types of Encoders
Priority Encoder
Decimal to BCD Encoder
Octal to BCD Encoder
Hexadecimal to Binary Encoder

## Slide 70: Priority Encoder
This is a special type of encoder.
Priorities are given to the input lines.
If two or more input lines are “1” at the same time, then the input line with highest priority will be considered.

## Slide 71: Priority Encoder 8:3
‘8’
inputs
‘3’
outputs
Priority
Encoder
8:3
Y2
D0
D1
D2
D3
D4
D5
D6
D7
Y1
Y0
Highest Priority
Lowest Priority

## Slide 72: Priority Encoder 8:3
Inputs |  |  |  |  |  |  |  | Outputs |  | 
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X | X | X
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | X | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | X | X | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | X | X | X | 0 | 1 | 1
0 | 0 | 0 | 1 | X | X | X | X | 1 | 0 | 0
0 | 0 | 1 | X | X | X | X | X | 1 | 0 | 1
0 | 1 | X | X | X | X | X | X | 1 | 1 | 0
1 | X | X | X | X | X | X | X | 1 | 1 | 1
Truth Table:

## Slide 73: Decimal to BCD Encoder
‘9’
inputs
‘BCD’
outputs
Decimal to
BCD
Encoder
A
D1
D2
D3
D4
D5
D6
D7
B
C
D8
D9
D

## Slide 74: Decimal to BCD Encoder
Inputs |  |  |  |  |  |  |  |  | Outputs |  |  | 
D9 | D8 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D | C | B | A
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | X | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | X | X | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 1 | X | X | X | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | X | X | X | X | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | X | X | X | X | X | 0 | 1 | 1 | 0
0 | 0 | 1 | X | X | X | X | X | X | 0 | 1 | 1 | 1
0 | 1 | X | X | X | X | X | X | X | 1 | 0 | 0 | 0
1 | X | X | X | X | X | X | X | X | 1 | 0 | 0 | 1
Truth Table:

## Slide 75: Applications of Encoders
Multiplexers: Converts parallel data bus to serial data stream for transmission or vice versa.
Communication Systems: Encodes digital signals for efficient transmission over limited bandwidth channels.
Keyboards and Scanners: Encodes key presses/scan lines into digital format.
Seven Segment Displays: Uses BCD encoders to display decimal numbers.
Barcode Readers: Decodes barcodes scanned as varying reflectance into digital data format.

## Slide 77
THANK YOU